## Slide 1: Mengwen He <mengwenh@andrew.cmu.edu> Emily ruppel <eruppel@andrew.cmu.edu> Iljoo Baek <ibaek@andrew.cmu.edu>
Wireless Sensor Network 18-748 March 8th, 2017
Gait Monitoring System
- SAFEWALK -

## Slide 2: Agenda
Problem / Solution / Use Case
System Configuration
Goals and Technical components
Demo Plans
Role & Responsibility
Schedule

## Slide 3: Problem
Elder Family Member
Physical Therapist (PT)
Family
Falls frequently
Lives with constant fear
Faces long-term medicalization

## Slide 4: Problem
Elder Family Member
Physical Therapist (PT)
Family
It would be very beneficial for me to know what activities my patients engage in outside of their therapy sessions. It is not enough for a patient to follow recommended exercises during their sessions if they do not practice them…

## Slide 5: Problem
Elder Family Member
Physical Therapist (PT)
Family
Little time with elder family member
Fearful of family member falling

## Slide 6: Solution
Measures Gait using wireless sensor network
Helps Doctor/Physical Therapist monitor patients
SafeWalk

## Slide 7
Stride length
Knee extension
Gait Measurement Parameters
Gait Speed, Cadence, Double Stance Time, Swing Time, Swing Time Variability, Cadence Variability, Chair Time Rise, Ability to do Tandem Stance, Lower extremity muscle strength
Notes: Add data source
Proprioception decreases and the muscles weaken

## Slide 8: Use Case
Hospitals
Nursing Homes
SafeWalk
Patients

## Slide 9: System Configuration
IMU
Firefly
IMU
Data Server
IMU | 6 EA
Firefly | 7 EA
PC | 1 EA

## Slide 10: 9-Axis IMUs Devices
Embedded IMU
Price: $50
Quantity: x6~4
Update rate: 100Hz
Built-in low-pass filter
Relatively low accuracy
Mount point: thigh + calf + (foot)
Price: $150
Quantity: x0~2
Update rate: 250Hz
Built-in Kalman filter
Relatively high accuracy
Mount point: (foot)

## Slide 11: IMU Data Process
Noise cancellation & Estimation
  Low Pass filter (a smoother)
  Kalman Filter (a tracker to fuse acc+gyro with mag)

## Slide 12: Multiple IMUs Calibration
Get IMUs’ Position & Orientation in a Unified Coordinate
  Visualization
  Gait data association

## Slide 13: Calibration Method
Calibration Target: Initial (T=0) Position & Orientation
(IMU)
(IMU)

## Slide 14: Calibration Method
Unified Coordinate for Calibration: Fixed Camera
(IMU)
(IMU)

## Slide 15: Calibration Method
Camera Based Calibration
(IMU)
Solution:
where is the visible time set
Keys:
Require tight time synchronization
Need as many paired data as possible
Need to handle IMU accumulated error
  Time-weighted LSE
Manually locate IMU on images
  CV track method is possible
  RANSAC to get rid of wrong data
Image
Camera
Projection Matrix
(3D  2D)
Invisible

## Slide 16: Data Communication
Master-to-slave
Packet loss detection
Synchronization
Data logging

## Slide 17: Gait Data Analysis
Gait Speed
Cadence
Stride Length
Double Stance Time
Knee extension
Swing Time
Stride Length Variability
Swing Time Variability
Cadence Variability

## Slide 18: Fabrication
Sensor Enclosure box Design & Fabrication

## Slide 19: Visualization
Visualization
  Data
  Motion (Extra work)

## Slide 20: Operating system
Firefly
IMU
Data server
…
Data Communication (Topology, Error recovery..)
Multiple IMU Calibration (Manual, Automatic)
IMU Data Process (Noise, Estimation etc.)
Gait Data Analysis
Visualization
Data Logging
Data Communication (Topology, Error recovery..)
Multiple IMU Calibration (Manual, Automatic)
IMU Data Process (Noise, Estimation etc.)

## Slide 21: Intermediate Demo
Implement entire pipe line with single IMU
Firefly
IMU
Data Server
Data Communication
Single IMU Calibration
Single IMU Data Process
Data Communication
Single IMU Calibration
Single IMU Data Process
Visualization (Single IMU)
Sensor node

## Slide 22: Intermediate Demo
Calibration with two IMUs

## Slide 23: Final Demo
Multiple IMU Calibration

## Slide 24: Final Demo
Live Real-time Demo
Real-time warning
  Gait-Change Detection
Shunsuke

## Slide 25: Role & Responsibility
EMILY
  Communication between nodes
  IMU to Firefly data transfer
  Gait pattern analysis
ALEX
  Multiple IMU Calibration
  IMU Data Processing
  Data transfer from master node to PC
ILJOO
  Gait pattern analysis
  Data visualization & logging
  Enclosure fabrication

## Slide 26: Schedule

## Slide 27: Project Website
https://17s-wsn-proj.github.io/Website/index.html

## Slide 28: Reference
Anatomical Calibration through Post-Processing of Standard Motion Tests Data
  http://www.mdpi.com/1424-8220/16/12/2011/htm
Gait Analysis Using Wearable Sensors
  http://www.mdpi.com/1424-8220/12/2/2255/htm
Symbolic Modelling of Dynamic Human Motions
  http://www.intechopen.com/books/biosensors/symbolic-modelling-of-dynamic-human-motions#
Assessment of walker-assisted gait based on Principal Component Analysis and wireless inertial sensors
  http://www.scielo.br/pdf/rbeb/v30n3/03.pdf
Gait and Foot Clearance Parameters Obtained Using Shoe-Worn Inertial Sensors in a Large-Population Sample of Older Adults
  file:///C:/Users/iljoo/Downloads/sensors-14-00443.pdf
Automatic pairing of inertial sensors to lower limb segments – a plug-and-play approach
  https://www.degruyter.com/downloadpdf/j/cdbme.2016.2.issue-1/cdbme-2016-0155/cdbme-2016-0155.pdf

## Slide 29: Q&A
Questions?

## Slide 30: Appendix : Bandwidth
Firefly x 6
IMU
Data Server
Firefly
Master
I2C
UART
IEEE 802.15.4
IEEE 802.15.4 : 250 Kbps = 32,000 bytes/sec
UART : 115,200 baud = 11,520 bytes/sec
One sample : 40 x 2 = 80 bytes
# of nodes : 6
 | Data Name | Data type | Size (byte)
ID | ID | unsigned long | 4
Sequence | Seq | unsigned long | 4
Raw Data | TimeStamp | unsigned long | 4
 | accelX | float | 4
 | accelY | float | 4
 | accelZ | float | 4
 | gyroX | float | 4
 | gyroY | float | 4
 | gyroZ | float | 4
 | magX | float | 4
 | magY | float | 4
 | magZ | float | 4
quaternion | qw | float | 4
 | qx | float | 4
 | qy | float | 4
 | qz | float | 4
Euler angle | pitch | float | 4
 | roll | float | 4
 | yaw | float | 4
Total |  |  | 76
IMU Freq (Hz) | Data (Bytes)
100 | 48,000
50 | 24,000
30 | 14,400
20 | 9,600
Bottle neck

## Slide 31: Appendix : Battery
2,800 mAH (@ 25ma) 1.5v x 2 (series)
Scenario 1: Firefly + Sparkfun 9DoF Razor IMU
  Firefly node : 24.4 mA (Active + TX)
  Sparkfun 9DoF Razor : 7.6 (Active)
    Invensense MPU-9250 : 3.8 mA (Active)
    Atmel SAMD21 : 3.64 mA (Active)
  Total power : 32 mA (~4 days)
Scenario 2: Firefly + 3-Space Embedded IMU
  Firefly node : 24.4 mA (Active + TX)
  3-Space Embedded IMU: 45 mA (Active)
  Total power : 70 mA (~1.5 days)

## Slide 32: Appendix : Purchase List
Items to be purchased
  Box Fabrication ($0)
  Straps (<$20)
  IMUs*) ($50 x 4 + $140 x 2 = $480)
  Battery (<$50)
  Total : ~$550

## Slide 33: Appendix : Use Case Example
posture training :
strength training :
SafeWalk
Data Center
PT Centers
Gait Trends
Risk
Recommended Therapy
NAME
Mary
AGE
65
SEX
F

## Slide 34: Appendix : Biz Model
Product
Service
Brand
Stand
Option
Customization

## Slide 35: Appendix : Biz Model
Fall Characterization
Softer Falling
Fall Prevention
Monitoring
Protection
Strength
DATA
DATA

## Slide 36: Appendix : Competitor